## Slide 1
Infrastructure monitoring
Marian Rychtecký
& NIX.CZ Dev team

## Slide 2
NX OS DME
What you get ?
Speed
  Requests takes milliseconds (full switch setup ~5s)
  Individual requests (interface, VLAN, VNI, BGP settings) ~100ms
  Reliability of the REST API
Operational parameters

## Slide 3
NX OS DME
(templates translating)
snmp-server contact email@domain.cz
snmp-server location Site 1, Prague, CZ
POST /api/mo/sys/snmp/inst.json
{
"snmpInst": {
"children": [
{
"snmpSysInfo": {
"attributes": {
"sysContact": "email@domain.cz",
"sysLocation": "Site 1, Prague, CZ"
}
}
}
]
}
}

## Slide 4
Collecting objects
"rmonIfIn": {
"attributes": {
"broadcastPkts": "3",
"clearTs": "never",
"discards": "0",
"dn": "sys/intf/phys-[eth1/5]/dbgIfIn",
"errors": "0",
"modTs": "2023-07-11T09:44:04.692+00:00",
"multicastPkts": "1995153",
"nUcastPkts": "1995156",
"noBuffer": "0",
"octetRate": "4947614883",
"octets": "60673271644077186",
"packetRate": "5404507",
"rateInterval": "300",
"ucastPkts": "63082941837541",
"unknownEtype": "0",
"unknownProtos": "0"
}
}
}

## Slide 5
Statistics in the real world
Traffic weather map
External Graphs
Internal Graphs
DME API
Influx API
Network device (Cisco Nexus 9300)
API
Netbox
Python
code

## Slide 6
Collecting data every 30s
Data pre-processing (calculated items)
Saving data to TSDB
Collecting objects

## Slide 7
Scale
We collect
        37 devices
        2339 interfaces
        63080 metrics

## Slide 8
Collection and storing
700ms to collect
250ms to store

## Slide 9
Data handling – InfluxDB 2
“main” bucket
~4GB / month
RAW data – 30s intervals
weekly bucket (17MB/w)
30 minutes AVG,MEAN,MAX
daily bucket (7MB/d)
5 minutes AVG, MEAN, MAX
monthly bucket (35MB/M)
2 hours AVG, MEAN, MAX
yearly bucket (~38MB/y)
1 day AVG, MEAN, MAX
Down-sizing tasks

## Slide 10
Data handling – InfluxDB 2
from(bucket: “main")
|> range(start: -task.every)
|> filter(fn: (r) => r["_measurement"] == "nx-stats")
|> aggregateWindow(every: 30s, fn: sum)
|> aggregateWindow(every: 1d, fn: mean)
|> set(key: "_measurement", value: "mean")
|> toInt()
|> to(bucket: “stat_year")
Flux script example

## Slide 11
Data handling – InfluxDB 2
weekly bucket
30 minutes AVG,MEAN,MAX
daily bucket
5 minutes AVG, MEAN, MAX
monthly bucket
2 hours AVG, MEAN, MAX
yearly bucket
1 day AVG, MEAN, MAX
main bucket
30 sec AVG, MEAN, MAX
Python HTTP API
Flux lang

## Slide 12
Data handling – InfluxDB 2
Visualization using uPlot

## Slide 13
Data handling – InfluxDB 2
Visualisation using uPlot

## Slide 14
Data handling – InfluxDB 2

## Slide 15
Weathermap using InfluxDB
API
Network device (Cisco Nexus 9300)
API
Netbox
Python
code
Influx DB
Weathermap template
Processed data with template variables
Python
HTTP API
Processing CDP, link speeds and loads

## Slide 16
Weathermap using InfluxDB

## Slide 17
Real life scenario - DDoS
Traffic bit/s
Discards p/s
Max 14.88G

## Slide 18
Real life scenario - DDoS
30s intervals averaged in 300s window

## Slide 19
Real life scenario - DDoS
30s intervals max in 300s window

## Slide 20
Real life scenario - DDoS
30s intervals maximums

## Slide 21
Real life scenario - DDoS
30s intervals maximums - zoomed

## Slide 22
(s)Flow analysis
sFlow
Network device (Cisco Nexus 9300)
API
Netbox
Python
code
Influx DB
Weathermap template
Python
HTTP API
FTAS

## Slide 23
(s)Flow processing
~150 Mbit/s of sFlow samples
downsizing tasks
5 min statistics for day - 700MB/week
30 minutes statistics for week
2 hours statistics for month
1 day statistics for year
Sankey diagram

## Slide 24
mr@nix.cz
Thank you for your attention.